## Slide 1: Application of Image Processing on enhancing the infrared image in Military
GROUP MEMBERS:
MUHAMMAD AMIRUL FAHMI BIN NOOR ANIM (B19EC0018)
MOHD ANAS BIN ADNAN (B19EC0043)
NUR HASANAH BINTI SARIDDON (B19EC0033)
SCSV 3213 FUNDAMENTAL OF IMAGE PROCESSING – sec 01
Dr. md sah bin hj salam

## Slide 2: Problem description
Recognition and identification range limiting the quality on infrared image
Problems that affected image quality:
Sensor - Quality depends on size of infrared director array and sensitivity
Intervening atmosphere - Scanning over long ranges impact on image quality

## Slide 3: Solution
Create TNO Image Enhancement System that consists of seven image enhancement techniques
Image enhancement techniques used:
Artifact reduction
Contrast enhancement
Dynamic super resolution
Stabilization
Stitching
Turbulence compensation
Automated detection

## Slide 4: Artifact reduction
A process of recovering a sharp image from degraded image
Scene based non uniformity reduction and bad pixel removal
Results in comfortable observation

## Slide 5: Local adaptive contrast enhancement (LACE)
The dynamic range of such imagery may exceed the display capabilities of standard display devices, resulting in the visualisation process losing information.
LACE is an algorithm for compressing the overall dynamic range of images while preserving small details of amplitude and maintaining an overall natural look.
Used only for displaying.
Two input parameters, the input noise and the degree of enhancement, are required by LACE.
The degree of change depends on the operator’s task.
Mild LACE will result in a natural picture, while medium LACE with lots of details will be less natural.
Example of the application of a mild version of LACE (next slide).

## Slide 6: Local adaptive contrast enhancement (LACE)
Before
AFTER

## Slide 7: Dynamic super resolution
Super Resolution is the generation of higher resolution imagery using resolution enhancement and image sharpening techniques
Basic mechanism behind the resolution enhancement is that temporal resolution of image sequences
Image sequences is exchange for spatial resolution while improving the signal to noise ratio.
Several recordings of the same scene are combined to a high-resolution image

## Slide 8: Stabilizing and motion estimation
The benefit of an accurate SBME algorithm is that no (expensive) external motion sensors are required.
Its motion model should match the real scene motion to achieve an effective SBME algorithm.
Since this accurate motion estimation is already carried out, it is possible to implement other techniques without much trouble, such as electronic stabilisation and mosaic generation.
A translation only or affine motion model would not be appropriate for certain military applications, including driver assistance applications: objects such as trees can have dramatically different motion patterns compared to their direct context due to the 3D nature of a scene and significant motion of the sensor.
Continue ->

## Slide 9: stitching
Image stitching is essential to generate large overview with camera
Image stitching generate a single image containing the image information from the entire scene when the individual image, panorama, or complete hemisphere are recorded in sequence of time.
Overlapping areas are used in smbe to determine the motion , so the interesting area and awareness will show to the operator

## Slide 10: Turbulence compensation
Atmospheric turbulence effects deteriorate imagery which is captured over long ground to ground ranges.
This diminishes the recognition ranges is important to compensate visual degradation due to atmospheric turbulence.
Turbulence compensation is challenging problem because the amount of turbulence is spatially varying due to an isoplanatic conditions.
The isoplanatic angle ,the angle which the turbulence can be assumed constant, varies with atmospheric conditions and the amount of turbulence varies significantly in time
When the turbulence conditions are stronger and the anisoplanatic angle is smaller the variations within and between the frames are larger and requires a local processing approach

## Slide 11: Automated processing
These scene modifications are intended to be used as moving target markers that can be used for Moving Target Detection (MTD) along with a proper tracking algorithm.
It is possible to use static scene components as SBME inputs, leading to an undisturbed estimation of motion.
First, automated processing may provide feedback on priorities and risks.
The next step is to analyse the threat's behaviour pattern, which offers valuable data on the threat’s intent.
Several strategies for developing knowledge are being pursued for military applications.

## Slide 12: Conclusion
Better observation over long range
Better observation in foggy and rainy conditions
Cost effective digital zoom in IR imaging
More effective use by operator by automatic detection and classification of specific objects
No operator efforts are required in setting camera/monitor settings

## Slide 13: MERIT
Piet B.W. Schwering , Rob A.W. Kemp, Klemur Schutte “Image Enhancement Technology Research for Army Applications
https://www.researchgate.net/publication/260670029_Image_enhancement_technology_research_for_army_applications
First page ‘Soldier’ icon made by Good Ware from www.flaticon.com