## Slide 1: Class Activity 3a: TYPE OF INTERFACES
PREPARED BY,
MAIZATUL AFRINA SAFIAH BINTI SAIFUL AZWAN A20EC0204
MADINA SURAYA BINTI ZHARIN A20EC0203
NAYLI NABIHAH BINTI JASNI A20EC0105
MADIHAH BINTI CHE ZABRI A20EC0074
NURFARRAHIN BINTI CHE ALIAS A20EC0121
SAFIRA NURUL IZZA A18CS0323

## Slide 2: TANGIBLE

## Slide 3: WHAT IS TANGIBLE USER INTERFACE(TUI)?
Moved from GUIs to TUIs in mid-1990s
TUIs use physical forms that fit seamlessly into user’s physical environment.
Key idea: Give tangible (physical) form to digital information
TUIs make digital information directly manipulatable with our hands and perceptible through our peripheral senses through its physical embodiment.

## Slide 5: TUIs Features
Tangible representation make information directly graspable and manipulable through haptic feedback.
Intangible representation (video projection) synchronizing with tangible representation

## Slide 6: First Generation TUIs
Urban Planning Workbench (Urp) uses scaled physical models of architectural buildings to configure and control an underlying urban simulation of light reflection, wind flow, and traffic congestions.
Urp and shadow simulation use physical building models that cast digital shadows and a clock tool to control time of day.
All tangible objects in Urp must be predefined (physically or digitally) and unable to change something while other process is ongoing. Thus, Tangible Media group design SECOND GENERATION (ORGANIC) TUI

## Slide 7: TUIs using printed paper markers

## Slide 8: Second Generation TUIs
Organic TUIs that utilize continuous tangible material (clay and sand) for rapid form sculpting for landscape design.
Examples: Illuminating Clay and Sand Scape
Flexible materials that integrate fully flexible sensors and displays shows great potential to express ideas in tangible form.
User insert any physical objects directly under the camera to understand highly complex topographies.

## Slide 9: TOUCH

## Slide 10: Touch User Interface?
Sense of touch (haptics) is used as computing-pointing mechanism.
Examples: Touchscreen on Smartphones & ATMs

## Slide 11: How does it work (touchscreen)?
Resistance
Consists of two different layers, the first layer made out of plastic that has conductive materials underside of it and the second is made up of glass or hard plastic which also includes coating of conductive materials.
The two layers were kept apart by a spacer.
When the screen is touched, first layer deforms so both conductive film meet, and by measuring the resistance of both layers at their point of contact, it is possible to get the accurate touched position.
Capacitive
A capacitor consists of two coated with conductive materials glass layers that separated by insulating material (usually air).
When a finger is close to a capacitor it changed the local electrostatic field. The system will constantly monitors the capacitors to detect the exact point of contact.
Due to the measurement points are discrete, it is possible to detect several fingers on screen at the same time.

## Slide 13: History of Touchscreen Technology
1960s - 1970s
The invention of touch screen and development of “touch sensor”
Invented by Eric A. Johnson that known as capacitive touchscreen. In 1970s, another design which is resistive touchscreen came
First Consumer Models and New Technologies
The first brand who first release product with touchscreens is Hewlett-Packard(HP) and the first machine that was created is called personal computer.
1980s
Popular Touchscreens
The possibilities of handheld devices, the first touchscreen smartphone with a calendar, address book, notepad and others.
1990s
Pre-Smartphone Touchscreens
Develop the first multi-touch gesture-based products such as keyboards.
2000s
Touchscreen Explosion
The application of this technology through different field such as in business.
Present

## Slide 14
Arduino Touchscreen Display using a resistive touchscreen