## Slide 1
Prepared by:
SUNG SHEAU HUI A18CS0248
NUR FATIN BINTI ROZADIN A18CS0191
SIFRA MANALU A18CS0327
UMI HAIZA BINTI MAHAMUD A18CS0270
SALMAN MOHAMED IBRAHIM AHMED IBRAHIM A18CS0356
CHAPTER 8
Differentiate between connection devices and services, including dial-up, DSL, cable, satellite, and cellular.
Describe data transmission factors, including bandwidth and protocols.

## Slide 2: DIGITAL SUBSCRIBER LINE (DSL )
DSL : Digital subscriber line is a family of technologies that are used to transmit digital data over telephone lines .

## Slide 3: DIAL-UP
Dial-up : internet service is a service that allows connectivity to the internet through a standard telephone line.

## Slide 4: DIFFERENCES BETWEEN DIAL-UP AND DSL
Comparison | DIAL-UP | DSL
Speed | Slow speed | High speed
Cost | Inexpensive | More expensive
Service | You can get service almost anywhere. | You need to be within a certain distance of the telephone company’s Central office.
Connection devices | You only need a computer with a modem to use it. | You need special equipment set up with a DSL connection.
From : https://www.quora.com/How-do-DSL-and-Dial-Up-internet-differ-from-each-other

## Slide 5
Twisted-Pair Cable | Coaxial Cable | Fiber Optic Cable
Consists of pairs of copper twisted together and covered by protective sheath (jacket). The twists important because: Cause the magnetic fields around the copper wires to intermingle, making them less susceptible to outside interference. Reduce the amount of crosstalk interference. Shielded twisted-pair (STP) cable contains a layer of foil shielding to reduce interference. Unshielded twisted-pair (UTP) doesn’t have the foil of shielding. | Still being used in some manufacturing facilities where machinery creates heavy electrical interference. Consists of: A core (usually copper), at very center. Solid layer of nonconductive insulating material surrounds the core. A layer of braided metal shielding covers the . An external jacket of lightweight plastic covers the internal cable components. | Composed of: A glass (or plastic) fiber (or a bundle of fibers called a core). A protective layer of glass or plastic cladding is wrapped around the core. Additional protection:- Outer jacket (sheath) which is often made of a durable material such as Kevlar (the substance used to make bulletproof vests. Data transmission can pass only in one direction.
CABLE
Factors that always need to be considered when choosing a cable type: Maximum run length, bandwidth, bend radius (flexibility), cable cost, installation cost, and interference.
Signals travelling down a cable are subject to two types of interference; Electromagnetic interference (EMI), Radio frequency interference (RFI).
From book Technology in Action, Twelfth Edition by Alan Evans, Kendall Martin and Mary Anne Poatsy. Pearson, 2016

## Slide 6
1. Your Device and the satellite Internet modem.
2. The satellite dish.
3. Satellite in space.
4. satellite internet service's hub
5. The information
SATLLITE CONNECTION SERVICE
From https://www.toptenreviews.com/services/articles/satellite-internet-101-how-does-it-work/

## Slide 7: CELLULAR SERVICE
A cell might use a different set of frequencies from neighboring cells, to avoid interference and provide guaranteed service quality within each cell.
The most common example of a cellular network is a mobile phone (cell phone) network. A mobile phone is a portable telephone which receives or makes calls through base station. Radio waves are used to transfer signals to and from the cell phone.
Cell
Base Station
From https://en.wikipedia.org/wiki/Cellular_network

## Slide 8: BANDWIDTH
Bandwidth is defined as a range within a band of frequencies or wavelengths. Bandwidth is also the amount of data that can be transmitted in a fixed amount of time.
For digital devices, the bandwidth is usually expressed in bits per second(bps) or bytes per second. For analog devices, the bandwidth is expressed in cycles per second, or Hertz (Hz).
The bandwidth is particularly important for I/O devices. For example, a fast disk drive can be hampered by a bus with a low bandwidth. This is the main reason that new buses, such as AGP, have been developed for the PC.
From: https://www.webopedia.com/TERM/B/bandwidth.html

## Slide 9: PROTOCOLS
It is how computer ‘talk’ to each other as each computer contains unique IP that built into the computer's operating system.
When two devices want to successfully communicate, they must agree to follow some rules about the way they will do it. These are known as protocols.
The two basic protocols used on the Internet are IP (Internet Protocol) and TCP (Transmission Control Protocol). Together, they are referred to as the TCP/IP.
From: http://theteacher.info/index.php/fundamentals-of-cs/3-data-transmission/topics/2652-the-importance-of-protocols-and-standards

## Slide 10: TCP/IP
Main suite of protocols used
TCP/IP Protocol Suite | Description
Internet Protocol (IP) | Sends data between computers on the internet
Transmission Control Protocol (TCP) | Prepares data for transmission and provide for error checking and resending lost data
User Datagram Protocol (UDP) | Prepares data for transmission; lacks resending capabilities
File Transfer Protocol (FTP) | Enables files to be downloaded to a computer or uploaded to other computers
Telnet | Enables user to log in to a remote computer and work on it as if sitting in front of it
Hypertext Transfer Protocol (HTTP) and HTTP Secure (HTTPS) | Transfer Hypertext Markup Language (HTML) data from servers to browsers; HTTPS is an encrypted protocol for secure transmissions
Simple Mail Transfer Protocol | Used for transmission of email messages across the internet
Dynamic Host Configuration Protocol (DHCP) | Takes a pool of IP addresses and shares themwith hosts on a network on as-needed basis
From book Technology in Action, Twelfth Edition by Alan Evans, Kendall Martin and Mary Anne Poatsy. Pearson, 2016

## Slide 11: PACKETIZATION
A packet of information
Created by the sending computer
Send to a router
The receiving computer
From book Technology in Action, Twelfth Edition by Alan Evans, Kendall Martin and Mary Anne Poatsy. Pearson, 2016