## Slide 1: HIGHWAY ENGINEERING [2832]
SYAHMI FIKRI BIN ZAINOOR LIZA
KHAIRUL NURATIQAH BINTI YAACOB
NUR ATIKAH BINTI MAT RAPI

## Slide 2
VISCOSITY TEST

## Slide 3
Viscosity test are used to measure the resistance to flow of bitumen.
Results are given in units of Poise (P), centistokes (cSt) or Pascal seconds (Pa s) as standard units of measurement, the relationship between these units depending on the specific gravity of the bitumen.

## Slide 4
Viscosity is simply a measure of a fluids resistance to flow and is described by the following equation:
where: | μ | = | viscosity (in cgs units of poise). poise = dyne-sec/cm2 = g/cm-sec (the SI unit of viscosity is the Pa-sec = N-sec/m2 = 10 poise)
 | τ | = | shear stress
 | γ | = | shear rate

## Slide 5
Asphalt binder viscosity is typically measured at 60° C (140° F) because it approximates the maximum HMA pavement surface temperature during summer in the U.S.
The basic absolute viscosity test measures the time it takes for a fixed volume of asphalt binder to be drawn up through a capillary tube by means of vacuum, under closely controlled conditions of vacuum and temperature (ASTM, 2001).
Although absolute viscosity is an improvement over the penetration test, it still only measures viscosity at one temperature and thus does not fully characterize an asphalt binders consistency over the expected range of construction and service conditions.
The standard absolute viscosity test is:
AASHTO T 202 and ASTM D 2171: Viscosity of Asphalts by Vacuum Capillary Viscometer

## Slide 7
PHOTO 5. Close up of two Cannon-Manning vacuum viscometers; flow is taking place in the left viscometer under vacuum

## Slide 8
PHOTO 6. Sample calculation for absolute viscosity

## Slide 9
Thank You…
be prepared for the next presentation…