## Slide 1: THE SYSTEM UNIT
FROM GROUP 2

## Slide 2: What is THE system unit ?
Part of a computer that houses the primary devices
Perform operations and produce results for complex calculations
Includes the motherboard, CPU, RAM and other components
The term system unit is generally used to differentiate between the computer itself and its peripheral devices, such as the keyboard, mouse and monitor.

## Slide 3
TYPES OF SYSTEM UNIT
DESKTOP
LAPTOP
WEARABLE
HANDHELD
TABLET

## Slide 4
COMPONENTS IN SYSTEM UNIT
MEMORY
SYSTEM BOARD
PROCESSOR

## Slide 5: SYSTEM BOARD
Core of the system (Mother Board)
Data path and traffic monitor
Common form factors are ATX (Advanced Technology Xetended), micro-ATX and mini-ITX
Contains a variety of electronic components such as sockets and chips
Additional system board are slots and bus lines

## Slide 6
ATX
Intel created the ATX form factor and first introduced it in 1995
-Integrated input and output ports
-Start Control by software
-3 Vol. from the source (reduces hardware cost, energy consumption, and heat)
-Have 6 expansion slots for things like graphics, sound, and network cards
-The size is 11.2 x 8.2 inch
Micro-ATX
Micro-ATX is also a standard for motherboards that was introduced in December 1997
-It is an evolution of ATX
-Its measures are 9.6 × 9.6 inch
- Smaller than ATX
-Micro-ATX supports up to 4 expansion slots
Mini-ITX
Developed by Via Technologies in 2001
-6.7 × 6.7 inches in measurement
-Low-power consumption motherboard
-Mini-ITX has just one expansion for a graphics card.

## Slide 7: Electronic component in the system board
Sockets
-the connection point for chips
-such as CPU socket
Chips
-Tiny circuit boards etched onto squares of silicon
-Also called silicon chip, semiconductor or integrated circuit
-Mounted on chip carriers

## Slide 8: Additional system board components
Slots
-Provide a connection point for specialized cards or circuit boards
-Provide expansion capabilities for the computer
-AGP slot, PCI slot and RAM slot
Bus lines
-Transfer data between the insides of a computer or between multiple computers
-To reduce the number of pathways communication travels.
-Have internal buses and external buses

## Slide 9: PROCESSOR
Engine of the computer or CPU
Microprocessor is a solid-state central processing unit
An integrated circuit that accepts coded instructions for execution
Have two types which are with pin and pin-less

## Slide 10: How does the processor work?
Does its primary work
A control center that converts data input to information output
Highly complex, extensive set of electronic circuitry that executes stored program instructions

## Slide 11: Difference between processor and microprocessor
Processor used to be in a separate box where data was fed to them and the result had to be collected from.
Microprocessor is used describe this arrangement of components on a single chip that includes other processors & these microprocessors don’t have RAM, ROM, and other peripheral on the chip.
Intel Pentium 4, Intel Core i7 or Ryzen 7- Microprocessor

## Slide 12
Processor
Basic component of CPU
Microprocessor chips
Multicore Processor
Coprocessor

## Slide 13: Basic Components of the CPU
Control unit -Tells the computer system how to carry out a program’s instruction
Arithmetic-logic unit (ALU) -Performs arithmetic and logical operations
The following diagram illustrates how instructions from a program are processed.

## Slide 14: Microprocessor chips
Chip capacities are expressed in word size
Word is the number of bits that can be processed at one time: 16, 32 or 64
Clock speed
- rate at which a microprocessor can complete a processing cycle

## Slide 15: Multicore processor
Single computing component comprised of two or more CPUs
Individual cores can execute multiple instructions in parallel
Increase performance of software
Quad-core supports 4 core processes

## Slide 16: coprocessor
designed to improve specific computing operations
entirely different circuitry that is designed to complement the central processing unit (CPU) of a computer
offload other processor-intensive tasks from the CPU in order to achieve accelerated system performance
Graphics Processing Unit (GPU) / Graphics coprocessors
Designed to handle a variety of specialized tasks such as 3D images, encrypting data and standardizing features in gaming computers

## Slide 17: memory
A component of a system unit
To store data, instructions and information
A work area of computer, where the CPU stores the data and instruction
Known as a main/primary/internal memory.
RAM (Random Access Memory), ROM ( Read Only Memory), flash memory and CACHE Memory

## Slide 18: What is RAM???
Gives applications a place to store and access data on a short-term basis
Stores the information in computer actively
SSDs (solid state drives) are also important components and will help our system reach its peak performance
Allow our computer to perform many of its everyday tasks
Allow our computer to switch quickly among these tasks

## Slide 19: RAM
Multiplexing and demultiplexing circuitry
Takes the form of integrated circuit (IC) chips with MOS (metal-oxide-semiconductor) memory cells
Associated with volatile types of memory
Volatile RAM are static random-access memory (SRAM) and dynamic random-access memory (DRAM)

## Slide 20: RoM
Read-only memory (ROM)
Information stored by the manufacturer
Non-volatile and cannot be changed
Retains its memory even after the computer turned off
CPU can read, or retrieve data and programs in ROM but the computer cannot change ROM

## Slide 21: Flash memory
Non- volatile memory chip
Combined features of RAM and ROM
Ability to be electronically reprogrammed and erased
Often found in USB flash drives, MP3 players, digital cameras and solid-state drives

## Slide 22: CACHE memory
Special very high-speed memory
Speed up and synchronizing with high-speed CPU
Buffer between RAM and the CPU
Reduce the average time to access data from the Main memory

## Slide 23: Expansion slots and cards
Any of the slots on a motherboard
To expand the computer's functionality
Video card, network card or graphic card
Expansion card is plugged directly into the expansion port

## Slide 24: Bus lines/ bus
Connect parts of the CPU to each other and various other components on the system board
Pathway for bits representing data and instructions
Bus width - Number of bits that can travel simultaneously down a bus
Architecture and design are tied to the speed and power for the computer
Have system bus and expansion bus

## Slide 25: Expansion bus
Expand the slot of motherboard
Provides additional features to a computer system
Include transferring information between internal hardware such as RAM
Expansion devices such as graphic cards or sound cards also included

## Slide 26: ports
Serves as an interface between the computer and other computers
Refers to the part of a computing device available for connection to peripherals such as input and output devices
To connect monitor, webcam, speaker or maybe mouse
Have two kind of ports
Standard ports
Specialized ports

## Slide 27: Standard ports
USB – keyboard, mice, printer or storage devices
Ethernet – High speed networking
HDMI (High Definition Multimedia Interface)- High definition video and audio
Thunderbolt – Provides high-speed connections
– Can connect up to 7 separate devices through 1 port

## Slide 28: Specialized ports
External Serial Advanced Technology Attachment (eSATA) - High-speed connection for external secondary storage
Musical Instrument Digital Interface (MIDI) - Connect musical instruments
Mini DisplayPort (MiniDP or mDP) - Connection to large monitors
VGA & DVI - Connections to analogue and digital monitors
FireWire - High-speed connections to FireWire devices

## Slide 29: cables
Used to connect external devices to the system unit via the ports
One end of the cable is attached to the device and the other end has a connector that is attached to a matching connector on the port

## Slide 30: Power supply
Computers require direct current (DC) power converting alternating current (AC) from wall outlets or batteries
Desktop computers have a power supply unit in the system unit
Laptops use AC adapters in the system unit
Tablets and mobile devices use internal AC adapters
Smartphones can use wire or wireless charging platforms

## Slide 31: Numeric Representation
Binary system consists of only two digits called bits
On = 1; negative charge
Off = 0; no charge
Byte = 8 bits grouped together
Hexadecimal system
Uses 16 digits
From 0 to 9 and A to F

## Slide 32: Character Encoding
Character encoding standards assign a unique sequence of bits to each character
ASCII - American Standard Code for Information Interchange
- Used by personal computers
EBCDIC - Extended Binary coded Decimal Interchange Code
- Used by mainframe computers
Unicode - New encoding due to explosion of the Internet
- Uses 16 bits
- Recognized by virtually all computer systems

## Slide 33: FUTURES
Computer manufacturers are still experimenting with alternatives to ATX
More and more programming language will be introduced
Most of the job will be taken over by the computer science field such as accountant, administration or even professional such as engineering will be taken over
Everything will be computerised as human is marching towards the AI (Artificial Intelligence) field

## Slide 34: Thank you and have a nice day